## Slide 1: Robotic Mapping into the Fourth Dimension - continued
Prof. Tom Duckett
Lincoln Centre for Autonomous Systems Research
School of Computer Science
University of Lincoln
Email: tduckett@lincoln.ac.uk

## Slide 4: Robots on patrol

## Slide 5
Notes: (2 out of 6 objectives)
O1: A unified understanding of space over time (WP1, WP4)
O2: Semantic segmentation of space (WP1,WP2, WP3, WP4, WP5)
  First level of abstraction towards symbolic representations

## Slide 6: Mapping & Localisation in CHANGING Environments – Approach 2: META-ROOMS

## Slide 7: Meta-Rooms
A volumetric-based method for re-creating the static structure of cluttered environments (“meta-rooms”).
Iterative improvement over time from partial observations
Segmenting clusters of dynamic objects
R. Ambrus, N. Bore, J. Folkesson and P. Jensfelt. Meta-rooms: Building and Maintaining Long Term Spatial Models in a Dynamic World. ICRA 2014 Workshop on Visual Place Recognition in Changing Environments

## Slide 8: Coloured 3D point cloud data
Down-sampled and filtered to remove noise

## Slide 9: Observations – input data
Pan-tilt sweeps at predefined waypoints
Red ellipses indicate missing sensory data
Filtering, boundary detection
Registration
Scans of the same room from 4 different days

## Slide 10: Meta-Room
Definition: the static structure of cluttered office environments
Created through an iterative process where dynamic elements are eliminated from the scene and previously occluded elements are added.
Once a meta-room has been created, dynamic elements can easily be extracted from new observations
Based on point cloud differencing:
P,Q – input point clouds, S – resulting point cloud, d – distance threshold

## Slide 11: Meta-Room Update
Current meta-room
New observation

## Slide 12: Meta-Room Update
Current meta-room
New observation
Occluded clusters
Green = deleted parts, Red = added parts

## Slide 13: Meta-Room Update
Current meta-room
New observation
Occluded clusters
Updated meta-room
Green = deleted parts, Red = added parts

## Slide 14: Dynamic clusters

## Slide 15: Dynamic clusters
Office chair
Pillow
Lamp
Office chair
PhD student on chair
Bicycle
Kitchen chair
Fruit basket

## Slide 16: Unsupervised learning of objects
Segment the dynamic elements into distinct clusters and re-identify them across observations.
Use appearance models, spatial distribution, and temporal behaviour
Significant improvement of the object detection rate compared to the original MetaRoom method.
R. Ambrus, J. Ekekrantz, J. Folkesson and P. Jensfelt. Unsupervised learning of spatial-temporal models of objects in a long-term autonomy scenario. Proc. IROS 2015.

## Slide 17: Mapping & Localisation in CHANGING Environments – Approach 3: FREQUENCY MAPPING

## Slide 18: A Frequency-based Approach to Robotic Mapping (FreMEn)
Explicitly models the environment's dynamics based on spectral analysis
Enables prediction of environment state at a particular time of day, based on history of past observations
T. Krajnik, J. P. Fentanes, G. Cielniak, C. Dondrup, and T. Duckett. Spectral Analysis for Long-Term Robotic Mapping. In Proc. ICRA 2014.
Notes: Amplitudes, phase shifts, frequencies

## Slide 19: Objectives
“Total recall”
  Security, assistive care, etc.
Compactness
  Online reasoning
Prediction
  What will happen at time t?
Novelty detection

## Slide 20: Temporal domain modelling
Classical world models neglect the temporal domain:
uncertainty of any state si is modelled by its probability pi
Including temporal aspect means that:
uncertainty of si (t) is modelled by probability pi (t)
However:
storing all observed si (t) and pi (t) is not feasible
Basic idea:
in days-to-months scales, si (t), pi (t) are quasi-periodic
represent pi (t) as superposition of harmonic functions
identify harmonic functions by Fourier transform

## Slide 21: FREquency Map ENhancement
T. Krajnik, J. P. Fentanes, G. Cielniak, C. Dondrup, and T. Duckett. Spectral Analysis for Long-Term Robotic Mapping. In Proc. ICRA 2014.
Notes: Amplitudes (influence), phase shifts (time offsets), frequencies (periodicities)

## Slide 22: Fourier Transform
See video

## Slide 23: Temporal domain model: example
Continuous observation of an office door (open/closed)
State s(t):
open/closed
Timescale:
one week
Measurements:
30Hz x 7 days
≈ 18 000 000

## Slide 24: Temporal domain model: example

## Slide 25: Temporal domain model: example

## Slide 26: Temporal domain model: example

## Slide 27: Temporal domain model: example

## Slide 28: Temporal domain model: example

## Slide 29: Temporal domain model: example

## Slide 30: Example 2: Topological Localization
Predict visual appearance of the environment and use the predicted model for topological localization
T. Krajnik, J. P. Fentanes, O. Mozos, T. Duckett, J. Ekekrantz and M. Hanheide. Long–Term Topological Localisation for Service Robots in Dynamic Environments using Spectral Maps. In Proc. IROS 2014.

## Slide 31: Example 2: Topological Localization
3D point clouds and RGB images of eight locations recorded every 10 minutes
Training:
  Model constructed using one week of data in 2nd week of Nov. 2013
  approx. 8000 observations, 35 km travelled
Testing
  One day in the next week (Nov. 2013)
  Another day in Feb. 2014

## Slide 32: Example 2: Topological Localization
Tested two types of place models:
  3D occupancy grids
    Matched using Hamming distance
  Visual descriptors
    BRIEF algorithm

## Slide 33: Example 2: Topological Localization
See video

## Slide 34: Example 2: Topological Localization
Spectral model learned during Nov 2013 was used
for localization on December 2013 and February 2014

## Slide 35: Example 3: Anomaly detection: Person presence
Anomalies
Location-specific model of person presence at three different locations

## Slide 36: Example 4: Time-dependent topological maps for motion planning
J. P. Fentanes, B. Lacerda, T. Krajnik, N. Hawes and M. Hanheide. Now or Later? Predicting and Maximising Success of Navigation Actions from Long-Term Experience. In Proc. ICRA 2015.

## Slide 37: Augmented Topological Map Representation
T=
Set of Locations
Action Between Locations
Set of Possible Actions
Function that maps an edge
between two locations to an
action
Is the set of probabilities of each edge being traversable at time t,

## Slide 38: Long-Term Deployment
Door
Experimental Deployment | 
Total Days | 76
Days of Activity | 35
Nodes In Topological Map | 17
Edges In Topological Map | 62

## Slide 39: Periodicity and Prediction Analysis
Signal
One Week
One Month
One Day

## Slide 40: High Level Motion Planning
Maximum Probabilities of fulfilling task (Fv1 V Fv14) at different dates and times of day

## Slide 41: Example 5: Spatio-temporal exploration of dynamic environments
Spatio-temporal exploration is a never-ending (life-long) process
The robot has to determine both where to go and when to go there
Our approach combines
  Spatio-temporal entropy
  Information-gain-based exploration
The CASAS-Aruba environment
T. Krajnik, J. Santos and T. Duckett. Life-Long Spatio-Temporal Exploration of Dynamic Environments. In Proc. ECMR 2015., Lincoln, UK.

## Slide 42: Spatio-temporal exploration

## Slide 43: Spatio-temporal exploration

## Slide 44: Spatio-temporal exploration

## Slide 45: Spatio-temporal exploration

## Slide 46: Spatio-temporal exploration

## Slide 47: Spatio-temporal exploration

## Slide 48: Spatio-temporal exploration

## Slide 49: Spatio-temporal exploration

## Slide 50: Spatio-temporal exploration

## Slide 51: Spatio-temporal exploration

## Slide 52: “4D” Spatio-temporal exploration
Information-driven map updates
  Spatio-temporal information-driven Next Best View.
  FreMEn occupancy grids + spatio-temporal entropy estimates + temporal path planning
  (Joao Santos’ PhD topic)

## Slide 53: “4D” Spatio-temporal exploration
FreMEn-based occupancy grid of the Lincoln Centre for Autonomous Systems (L-CAS) office. The static cells are in green and cells that exhibit daily periodicity are in red.
T. Krajnik, J. Santos and T. Duckett. Life-Long Spatio-Temporal Exploration of Dynamic Environments. In Proc. ECMR 2015., Lincoln, UK.

## Slide 54: Conclusions
World model that takes into account the dynamics of the environment from a long-term perspective.
We represent state changes using periodic functions, identified by means of the Fourier transform.
FREMEN is suitable for different timescales with constant memory requirements.
Can extend any world model with binary states, e.g. gridmaps (Octomap), landmarks and semantic maps
Compression ratios 1:106, prediction accuracy 95%.
Localization failure rate halved even after three months.

## Slide 55
Thank you for your attention.
Questions ?

## Slide 56: RELATED WORK

## Slide 57: Related Work
Hierarchical Object Maps (Anguelov et al. 2002)
SLAM with Detection And Tracking of Moving Objects (Wang and Thorpe, 2002)
  partition the static elements from the non-static elements, and consider each set separately.
  cannot handle long-term changes

## Slide 58: Related Work
Temporary Maps (Meyer-Delius et al., IROS 2010)
  model the effect of temporary objects by performing local SLAM
  localization with particle filter using these locally static maps

## Slide 59: Related Work
Independent Markov Chain Occupancy Grid Maps (Saarinen at al., IROS 2012)
  independent Markov chains (iMac) stored with every cell on the grid

## Slide 60: Related Work
Rao-Blackwellized Particle Filter with Hidden Markov Model (Tipaldi et al., 2013)
Dual –timescale NDT-MCL (Valencia et al., 2014)
  Short-term map
  Static map
Episodic Non-Markov Localization (Biswas & Veloso, 2014)
  Reasoning About Short-Term and Long-Term Features